## Slide 1
1958: The American satellite Vanguard 1 is launched. It was the first satellite with a solar PV power system.
Sputnik II satellite in 1957, was already powered with silicon cells.
https://www.nrel.gov/docs/fy04osti/33947.pdf
Alexandre-Edmond Becquerel discovered the photovoltaic effect, that is, the conversion of photons to electrons. Becquerel placed two platinum electrodes in a container filled with an electrolyte and measured that the current flowing between the electrodes increased when the setup was exposed to sunlight.
1839
William Adams and Richard Day proved that a selenium rod connected to platinum electrodes produced electricity when it was illuminated. This was the first observation of the photovoltaic effect in solids.
1876
1883
The inventor Charles Fritts built a small array of selenium cells with a total area of 30 cm2 and achieved an efficiency close to 1%.
Albert Einstein presents his quantum theory. Einstein explains the photoelectric effect by assuming that the light energy is being carried with quantized packages of energy that we call photons.
1905
1916
Jan Czochralski invented a method to grow high-quality crystalline materials. The method is still used today (see Chapter 5).
William B. Shockley, the coinventor of the transistor, explains the principles of operation of the PN junction. PV solar cells are developed during this decade at Bell Labs.
1954
Daryl Chapin, Calvin Fuller, and Gerald Pearson in the Bell Labs presented the first silicon solar cell with an efficiency of 6% and an area of 2 cm2.
In the same year, a thin-film heterojunction solar cell based on Cu2S/CdS attaining also 6% efficiency was developed at Air Force based (USA)
The first satellite with a solar PV power system (NASA Vanguard 1) was launched. The Russian satellite Sputnik 3 launched the same year also included solar cells.
1958
1950
Shockley and Queisser published a scientific article in which they calculated the maximum theoretical efficiency that can be attained by a solar cell. The Shockely-Queisser limit is presented in Chapter 6.
1961
Bell Labs launches the first solar-powered telecommunications satellite (Telstar).
1962
Photoelectric and photovoltaic effects are related, but they are not the same. In both cases, light is absorbed, and it causes the excitation of an electron to a higher energy level. We refer to the photoelectric effect when the electron is ejected out of the material, and to the photovoltaic effect when the excited electron is still contained within the material.

## Slide 2
Todelo PV es de 1994, casi 12 años después de la de California
A group at Ioffe Institute in San Petersburg led by Alferov developed a solar cell based on gallium arsenide heterojunction. The main benefits of GaAs cells were their high efficiency and resistance to the ionizing radiation in space.
1970
Geopolitical reasons triggered the two oil crises where the prices of oil skyrocketed. Populations and governments become more aware of the vulnerability of the oil economy and significant efforts were made to develop alternative energy sources. It is in this period that many solar research labs and institutions were founded.
70’s & 80’s
The first solar-powered pocket calculators and watches arrive on the market.
Solar PV covers 20% of the annual electricity demand in California.
2020
1973
1979
Cumulative global PV capacity reaches 1 TW
2022
NASA launched the first Orbiting Astronomical Observatory powered by a 1kW PV array.
1966
Cumulative Global PV capacity reaches 1 GW
1990
Germany launched the “1000-roofs” program aiming at installing 1000 domestic solar PV systems. This marks the beginning of policy support for PV.
1991
1981
First 350 kW Concentrator-PV array installed in Saudi Arabia
1982
First 1 MW utility-scale PV power plant with Arco Si modules on 2-axis trackers installed in California
1987
The Spanish company Isofoton manufactures and install bifacial PV panels
1994
GaInP/GaAs 2-terminal multijunction solar cell attained efficiency >30% (NREL, USA)
1985
Silicon solar cell attained efficiency >20% under standard sunlight (UNSW, Australia) and >25% under 200X concentration (Stanford)
Primera thin film
Avion solar
Solar race / solar decathlon